## Slide 1: Stability Test Strategy
Zha Xinjian
2015.03.02

## Slide 2: Agenda
Why Stability Test
MTBF target
Test Phase

## Slide 3: Why Stability Test
From Technique View, find deep/potential issues such as Memory Leak
User Experience will be better, as Most Frequent APPs will not have Force Close, ANR, Crash, or Reset

## Slide 4: Feature Stability
Objective:
  To Find device reboot, lock ups
  To Find APP Force Close, ANR
Test Strategy:
Device to perform many tasks (looping) over a period time to arrive at a Mean Time Between Failure (MTBF) for the device under test (software and hardware combination).

## Slide 5: Data Stability
Objective:
  To ensure the mobile handset can transmit data in the uplink & downlink without any resets or lockups in PC tethering/BT/Mobile Hotspot
Test Strategy:
Using VBScript loop to upload/download file to/from FTP Server, loop time shall be > 15hours or 30 Hours

## Slide 6: Feature Stability Test Function List
Telephony Stability Tests | Telephone
Messaging Stability Tests | SMS, MMS
Email Stability Tests | Email
Browser Stability Tests | Browser
Store Front / Download Stability Tests | Store
PIM Stability Tests | Calendar, alarm
Multi-Media Stability Tests | Camera , video, SoundRecorder, streaming, music player
Multi Tasking Stability Tests | Make a phone call, Start a browser session and load home page.
Menu Navigation Stability Tests | Launcher
Wifi Stability Tests | Wifi

## Slide 7: Feature Stability MTBF Target (5 devices)
Level 2
Level 1
LE: 400H TA: 600H
LE: 300H TA: 400H
Pass Rate for every module SHOULD >=95%
Valid MTBF for single DUT(Device Under Test) MUST >=40 H

## Slide 8: Feature Stability MTBF Practice Tips
Operator own standard Preferred
Project with specific req for Level 2 (LE 400/TA 600 for 5 devices)
Project without specific req or GL Project applies Level 1 (LE 300/TA 400 for 5 devices)
Numbers of DUT:
  Projects with New Platform: 5 DUTs
  Projects Followed: 3 DUTs

## Slide 9: Data Stability MTBF Target
Level 1
Level 2
15 Hours upload
15 Hours download
by WIFI Tethering
30 Hours upload
30 Hours download
by WIFI tethering

## Slide 10: Data Stability MTBF Practice Tips
Operator own standard Preferred
Project with specific req for Level 2 (30 Hours UL/DL for 1 device)
Project without specific req or GL Project applies Level 1 (15 Hours UL/DL for 1 device)
Numbers of DUT
  Projects with New Platform: 1 DUT
  Projects Followed: N/A

## Slide 11: Test Phase
Mockup
Proto
PIO
Lot
SW Alpha
SW Homo/LE
1st Round
2nd Round
TA
Homo 1
Stability
Homo 2
MR
1st Round+2 W
2nd Round+1W
Data Stability

## Slide 12
Thank You !